## Slide 1: AIT
~10 slides
Propose a design of the Electric Ground Support Equipment (EGSE);
Propose a design of the flatsat that will aid in the development of flight software and the verification of operations. Flatsat can be used for:
  Test and verify all hardware interfaces
  Verify all spacecraft modes and state transitions
  Test and verify software commands and procedures
  Validate Mission Operations commands and procedures
  Validate power transmission for operating modes
  Test for failure modes and recovery procedures
  Validate ground segment protocols and communications functionality
Propose CubeSat test plan including safety and handling procedure
Present the laboratory environment for spacecraft integration and tests

## Slide 2: AIT
Electric Ground Support Equipment:
  Goal: Design the equipment and software needed to test a CubeSat / FlatSat with little human interaction.

## Slide 3: AIT
EGSP:
  Acknowledged that antenna release mechanism testing is critical*
  It also has moving parts and will require some human interaction for verification that it will NOT damage the surrounding components.
  Heavy emphasis on testing starting mechanism when designed for maximum safety assurance*
  The other components will be designed to be modularly tested.

## Slide 4: AIT
Red = Will Become Flight Hardware
Black = Can be cheaply prototyped (not flight hardware right away)

## Slide 5: AIT
EGSP:
  SDR Transceiver (USRP B210 if available)
  SDR Transceiver (MegaBEE cube)
    70MHz-6GHz
    56MHz bandwidth per channel
    23dBm output Power
    -94dBm receiver sensitivity level
    Software: HDL,Matlab/Simulink,C/C++/Python
    USB V2.0 connection
    SMA antenna connectors
    FREE, Already in lab (good for rapid prototyping)
Notes: Note that the USRP is going to be purchased but that will not stop our prototyping! I have asked jayshri and we are able to make use of the MegaBEE cube that we have in lab (we have other SDR’s as well)

## Slide 6: AIT
CubeSat Test Plan:
  Safety and Handling Procedures:
    BBM:
      Summer student work 2019 + Capstone 2018 prelim
    Demonstration model:
      FlatSat
    Structural and Thermal Model:
      Bus redesigned, Need to do another thermal + vibe test
    Proto-Flight Model:
      FlatSat will turn into it
    Flight Model:
      From Proto-Flight Model

## Slide 7: AIT
People Resources:
  CubeSat Club members during the year.
    Will be started this year!!
    Safety training, bringing up to speed on project
    Assembly and Integration training
    Extra hands on demonstration model under team leads
  Capstone Teams:
    Structural and Thermal model
    Groundstation design
    PCB Design for custom boards
      Including inspection protocols, manufacturing plan and testing plan

## Slide 8: AIT
People Resources:
  Team Leads:
    Individual subsystems
    Develop a detailed testing plan if not done already.
  Summer Students(2019):
    Documentation is done (Github and Sharepoint)
    Assembly instructions for CubeSat bus
    Assembly instructions for assembling solar panels

## Slide 9: AIT
Still to do:
  EMI testing plan, requirements and procedure
    Identify resources required
  Custom board design + testing
  Request For Deviation form for early turn on of camera
    Timer circuit based on above decision
  Antenna release mechanism and testing
  Operations protocols and training with CubeSat club students

## Slide 10: AIT
Laboratory Environments for Spacecraft Assembly:
What class of clean room necessary?
Is air handling necessary?
Options for rooms:
  Thomson Engineering Building room 6
  Optics Lab Spencer Engineering Building room 3025A
  Western NanoFabrication Facility