## Slide 1
Western University – Nunavut Artic College
CubeSat Mission
Claire Lizotte, Matt Cross, Jayshri Sabarinathan
Department of Electrical and Computer Engineering
Introduction
What is a CubeSat?
  A CubeSat is a small satellite in the shape of a cube, each cube unit measure 10 cm x 10 cm x 10 cm. There can be up to 24 units per CubeSat system.
Our Mission:
  1. To provide learning and training opportunities for students in spacecraft development and operations and STEM outreach.
  2. Integrate and operate the Canadensys Nano VR camera into a 2U CubeSat.
The next step in the mechanical design would be to build a structural prototype and test it on a shaker table, as per the Nanoracks specifications to confirm the FEA analysis.
Conclusion
The structural design should be adequate, considering there is minimal displacement according to the FEA model. The Von Mises stresses are less than the tensile strength of Al 6061, so the supports should not fail. The mechanical design is able to accommodate all components while staying within the mass budget and meeting the center of mass requirements.
The mechanical design was created based on the specifications from Nanoracks, the launch provider.
The components that needed to be integrated into the CubeSat were selected by the capstone teams that worked on the project this school year. The structure had to be designed such that the components had the support they required and there was adequate space for the wires and harnessing.
Some of the challenges involved in the mechanical design included:
  Ensuring the center of mass is within 1 cm of the geometrical center of the CubeSat.
  Having the magnetorquers as close to the center of mass as possible.
  Assuring enough space for the wires and their bend radii.
Mechanical Design
Next Steps
Additional research involved investigating the deployment switch circuit, creating an system interface document, and exploring antenna deployment.
Furthermore, magnetorquers for the attitude control system were designed.
Other Work
Antenna
Camera
Transceiver
On Board
Computer
Engraving
Magnetorquers
GPS Transceiver
Battery
Camera
FEA Results
FEA Methods
The model was simplified by swapping components such as the on board computer and battery for dummy masses. The mass of the dummy components was slightly above the mass of the actual components, to account for the mass of the wires that would be attached to the components.
The model was quartered to allow the simulation to run with a finer mesh, which was critical as the structural components are only 3 mm thick. A curvature mesh was used since it mapped the element size to the features. The minimum element size was 0.5 mm.
The ends of CubeSat were fixed, as it would be in the deployer, and the gravitational loads were applied, as per the Nanoracks Deployer Interface Document.
CubeSat Stack
Factor of Safety Displacement Von Mises Stresses
This work was funded by a generous donation from Bill and Barbra Etherington. The CubeSat project is funded by the Canadian Space Agency’s Canadian CubeSat Project Grant, with king contributions from Canadensys Aerospace.
The factor of safety is greater than 100 wherever there purple. The grey areas are materials that are not Al 6061. The lowest factor of safety was 1.7, however this was on a the dummy mass for the camera and not on the structure, so it was deemed to be acceptable. This is also shown in the Von Mises plot, as it can be seen that the stresses are low over most of the structure. There are stress concentrations near the bolt holes in the rails. The maximum displacement of the structure is 0.0933 mm, which is acceptable.
Acknowledgements